## Slide 1: OpenDSS Training Workshop
Roger C. Dugan
Davis Montenegro
EPRI Knoxville, TN
September 24-25, 2019
Idaho Power Co.
Boise, Idaho

## Slide 2: 3. Scripting Basics – Large Circuits

## Slide 3: Scripting Large Circuits
For small circuits, it is often sufficient to put all the scripts in a single file
  Many of the IEEE test feeder examples are mostly in a single file
When you have large amounts of data, a more disciplined approach is recommended
Redirect Command
  Redirects the input to another file
  Returns to home directory
Compile Command
  Same as Redirect except repositions home directory

## Slide 4: The OpenDSS Main Screen
Selection to execute
Main Script Tab never goes away. Put some frequently-used commands here.
Solution Summary and Results
Results Text Box
Tabs for script files
Active Script file

## Slide 5: Using the Main Screen
You can switch between tabs and execute pieces of code from one window and then another
OpenDSS is always running and remains in the state after the last command until you tell it to do something else
OpenDSS.exe saves all windows on the main screen
  They appear where you left them when you shut down
  The next time you start up, you can resume your work
Values are saved to the Windows Registry

## Slide 6: OpenDSS Registry Entries
Certain persistent values are saved to the Windows Registry upon exiting the program
Default Editor Setting
After Redefining

## Slide 7: Organizing Your Script Files

## Slide 8: A Common Sense Structuring of Script Files
Run_The_Master.DSS
Master.DSS
LineCodes.DSS
WireData.DSS
LineGeometry.DSS
Spectrum.DSS
LoadShape.DSS
Libraries
Put a “Clear” in here
Transformers.DSS
Lines.DSS
Loads.DSS
Etc.
Circuit Definition
“Compile” the Master file from here
Make a separate folder for each circuit

## Slide 9: Organizing Run Scripts
Compiles the Circuit Description
Override Some Property Settings and/or Define Some Additional Circuit Element
Change an option
Solve Snapshot Power Flow
Selected Results Display
Based on 123-bus IEEE Test Feeder

## Slide 10: Organizing Your Master File
So Compile Doesn’t Fail
General Library Data
Circuit Elements for this Model
Let OpenDSS Define the Voltage Bases
(You can do this explicitly with SetkVBase command)

## Slide 11: Example: IEEE 8500-Node Test Feeder
Load and exercise the IEEE 8500-Node Test Feeder Circuit – an example of a large circuit

## Slide 12: Location of the IEEE 8500-Node Test Feeder Files

## Slide 13: Master File for IEEE 8500-Node Test Case

## Slide 14: Snippets of Circuit Script Files (they are large)

## Slide 15: Circuit Plot
Plot Circuit Power Max=2000 dots=n labels=n C1=Blue 1ph=3

## Slide 16: Voltage Profile Plot
Plot profile phases=all
Secondary Drops